## Slide 1
Data-Driven Corrosion Inhibitor Modeling
Pipeline Progress Report

## Slide 2
Goal & Context
Objective
Build a predictive model for Inhibition Efficiency (IE) to optimize inhibitor structures and dosages.
The Dataset
•
~300 Lab Runs: Comprehensive experimental data.
•
Key Descriptors: Formulation (C#, Mw, HLB, EO) & Conditions (Conc, pH).
•
Strategy: Dual-file approach (Original vs. Fixed pH 4.9) to isolate sensitivity.

## Slide 3
Preprocessing & Cleaning Workflow
Cleaning
Removed redundant columns, duplicates, and empty rows. Normalized "Unnamed" entries to ensure data integrity.
Calculation
Applied domain logic: IE = IE × AA / 100. Rescaled Inhibition Efficiency using Active Agent (AA) factor.
Splitting
Partitioned into Train (70%), Validation (15%), and Test (15%) sets. Applied train-only mean imputation and standard scaling.

## Slide 4
Exploratory Data Analysis: Distributions
Key Findings
•
C#, EO, and Mw Skew: C#, EO, and Mw all show strong right-skewed distributions with a few very high values, indicating potential outliers and suggesting that log-scaling or robust estimators may be beneficial in downstream modeling.
•
pH as a Discrete Factor: pH appears only at a few distinct levels (≈2, 4–5, and 11–12), supporting its treatment as a categorical design factor rather than a continuous variable in the current experiment.
•
HLB and IE Spread: HLB spans a broad range (≈3–22) while IE covers nearly the full performance window (≈−50% to 95%), confirming that the design explores both formulation space and response space sufficiently for capturing nonlinear relationships.

## Slide 5
Exploratory Data Analysis: Correlations
Pearson Correlation Insights
The heatmap reveals critical linear relationships:
•
Positive Correlation: Carbon Number (C#) shows a slight positive link to IE (~0.17).
•
Negative Correlation: Concentration (Conc) negatively correlates with IE (~ -0.16).
•
Non-Linearity: Weak linear correlations across other features suggest complex, non-linear interactions that simple models may miss.

## Slide 6
Feature Engineering & Loaders
Canonical Feature Set
We have locked the feature list for consistency across all models:
Pipeline Infrastructure
features.load_splits(): A centralized function that pulls pre-processed (X_train, y_train) triples.
Automation: Automatically regenerates processed CSVs if missing, ensuring downstream scripts remain clean and stateless.
•
Carbon Number (C#)
•
Molecular Weight (Mw)
•
HLB Value
•
Ethylene Oxide (EO)
•
Concentration (Conc)
•
pH Level

## Slide 7
Baseline Model Performance (R²)
The huge gap between Random Forest and Linear Regression confirms strong non-linear effects.
Random Forest (Val)
Random Forest (Test)
Linear Reg. (Val)
Linear Reg. (Test)

## Slide 8
Feature Importance Ranking
pH Level
Molecular Weight
Ethylene Oxide
Concentration
Carbon # / HLB

## Slide 9
Project Roadmap
Model Selection
Compare Gradient Boosting, Elastic Net, and SVR. Tune hyperparameters for both original and constant-pH scenarios.
Evaluation
Report MAE/RMSE metrics. Generate SHAP plots to interpret complex non-linear feature interactions.
Optimization
Translate the best performing model into a tool for recommending optimal inhibitor structures and dosages.